# Miniband

Type: Musical instrument
Difficulty: Medium
Time: 2 sessions
# Introduction
Make your own band! You'll get to create some musical instruments from a few simple electronic parts and plug them into your Rasperry Pi. You can then make beautiful music. Or a dreadful racket.
# Resources
This project needs quite a few bits to make all the instruments. You'll need:
- 3 Arduino boards, each with a USB cable
- 3 breadboards
- 1 x strip potentiometer (for the guitar)
- 2 x tilt sensors (for the maracas)
- 4 x piezo buzzers (the type in greetings cards) (for the drum kit)
- 7 × 10KΩ resistors
- Jumper leads, including some long female-female ones for connecting instruments to breadboards
- USB hub
- Plasticine (or some other modelling material, such as Sugru)
- Card
- Electrical tape
- Plastic drinking straw
- Pencil
- Coloured pens (optional)

# Overview
This project is complicated and there are few parts you need to build. This is how they all fit together.

Each instruments has its components plugged into a breadboard and connected to an Arduino. The Arduinos are connected by a USB cable to the USB hub, which is plugged into the Raspberry Pi. Each Arduino has a small program on it that detects when the instrument is played and sends a signal, via the USB cable, to the Pi. A small Python program on the Pi reads those messages and translates them into a form that Scratch and understand. The Scratch project reads the signals and plays the sounds, and does some cool animation as well.

We'll make one instrument work first, then add the others. Getting the first instrument working takes quite a while; the others are a lot quicker.
# Step 0: Install the resources you'll need
This step may already be done. Your helper will tell you if you need to do it.
1. Open a terminal window on the Raspberry Pi and run these commands:

   sudo aptitude update
   sudo aptitude full-upgrade
   sudo aptitude install arduino python-serial

   That will install the Arduino programming environment and the libraries that allow Python to read data from the Arduinos.
2. Copy the Miniband resources into the (new) directory /home/pi/codeclub/miniband
# Step 1: Make the Maracas
## You will need:
Arduino
Breadboard
2 tilt switches
long female-female jumper leads
various other jumper leads
Two 10KΩ resistors
Straw
Plasticine

## Wire up the maracas
1. Connect each tilt switch to two long female-female jumper leads. Connect ordinary male-male jumper leads at each end.
2. Use a jumper lead to connect the +5V and GND pins on the Arduino to the breaboard.
3. Plug one end of each maraca into the breadboard, next to the +5V lead
4. Connect two 10KΩ resistors[1] across the gap in the cenre of the breadboard
  [1] This is a pull down resistor. In the absence of any other input, it will make the output of the potentiometer (the centre pin) be at zero volts, which will read zero. All the instruments will have them, to ensure that they read zero when not being used.
5. Plug the end of the other maraca leads into the breadboard on the same row as the resistor.
6. Use another jumper lead to connect between near the resistor and pins 6 and 7 on the Arduino.
7. Wire in the other jumper leads following the diagram below

## Install the Arduino code
Open the Arduino environment on the Raspberry Pi and add this script:

int newState;
int states[] = {-1,-1};
const int pins[] = {6, 7};
const int wait = 500;

void setup() {
  for (int i = 0; i < 2; i++) {
    pinMode(pins[i], INPUT);
  }
  Serial.begin(57600);
}

void loop() {
  for (int i = 0; i < 2; i++) {
    newState = digitalRead(pins[i]);
    if (newState != states[i]) {
      Serial.println("maracas,1023");
      states[i] = newState;
      delay(wait);
    }
  }
}

Note the use of the states array to record whether the tilt switches were open or closed just now. The script will only send a message if the switches change.
Save the script
Upload the script to the Arduino

<test your project>
Open the serial port monitor in the Arduino environment and shake the tilt switches. Do you get messages when you move one of the switches? Do the readings stop when you stop moving them?
## Assemble the maracas
1. Cut two lengths of straw and put a large blob of Plasticine on one end of each.
2. Slide the tilt switch into the straw and push it into the plasticine so it sticks.

<test your project>
Open the serial port monitor again if you closed it earlier. Do the maracas still work? Do you get messages when you move one of the switches? Do the readings stop when you stop moving them?

# Step 2: Add the Arduino/Scratch translator reader
This is a complicated piece of Python that does a very simple thing. Basically, it monitors a bunch of USB ports and listens for any signals from them. If it reads a signal one one, it translates it and sends it on to Scratch.

Download it from the Code Club website to somewhere on the Raspberry Pi.

Change the DEVICES = line at the top of the script to refer to your Arduino. It might be
DEVICES = ['/dev/ttyACM0']
or
DEVICES = ['/dev/ttyACM2']
depending on what you've plugged in.

Don't run this script yet: it wants to connect to Scratch as well as the Arduino, and we've not done that bit yet.

<box>How do I know what the Raspberry Pi thinks my Arduino is called?
The Raspberry Pi gives each Aduino device a name when it's plugged in. Both the Arduino programming environment and the Pyhon translator need to know these names.
The Arduino tool shows you a list of available devices in the Tools | Serial Port menu.
The other way to find out is to open a terminal window, plug in the Adruino, and they type

dmesg

and look at the output. You should see something like

and “/dev/ttyACM0” is your Adruino.
</box>
# Step 3: Create the maracas player in Scratch
1. Start a new Scratch project.
2. Change the sprite to have the miniband/maracas costume (you may want to make it smaller). Import the miniband/maracas sound. You can delete the existing cat costumes and the meow sound.
3. Open the "Sensing" palette and right-click on the [slider] sensor value block at the bottom. Select the "Enable remote sensor connections" on the menu that pops up. This allows Scratch to listen to the Python translation script.
4. Now start that script. Open a terminal window and type
   cd ~/codeclub/miniband
   python music-maker-handler.py

   You should get some output that looks like this

   INFO:root:Connecting to Scratch...
   INFO:root:Connecting to Scratch
   INFO:root:Connected to Scratch
   INFO:root:Started listener on port /dev/ttyACM0
   INFO:root:Listeners running....
   INFO:root:Instrument: maracas, Value: 1023
   INFO:root:broadcast maracas
   INFO:root:Instrument: maracas, Value: 1023
   INFO:root:broadcast maracas

   The last two lines will repeat every time you move the maracas.

<test your project> Shake the maracas. Do you see extra "broadcast maracas" lines when you do?

Go back to Scratch and in the Control palette you should see a when I receive [maracas] hat block. Use that to make this script:

<test your project> Double-click on the maracas script in Scratch. Do you hear the sound? Now shake the maracas instrument you made. Do you hear the sound? Does you still see extra "broadcast maracas" lines when you shake them?
# Step 4: Create the drum kit
You will need:
Arduino
Breadboard
4 piezo-electric speakers
Four 10KΩ resistors
Plasticine
Straw
Card

## Wire up the drums
Piezo-electric crystals change shape when an electric current is sent through them. This makes them work as simple loudspeakers. But if you change their shape (by tapping them), they make an electric current. We'll use that current to signal that a drum has been hit. Because the speakers generate their own power, we don't need to supply any from the Arduino.
1. Use a long jumper to connect the GND pin on the Arduino to the ground rail on the breadboard.
2. Connect a jumper between the ground rail and a row of the breadboard.
3. Connect the black lead of the speaker to the same row.
4. Connect a 10KΩ resistor between that row and one nearby.
5. Connect the red lead of the speaker to this second row.
6. Connect a long jumper from this second row to pin 8 on the Arduino.
7. Repeat steps 2 to 6 for the other three speakers, connecting them to Arduino pins 9, 10, and 11.

## Install the Arduino code

const int NUMBER_OF_DRUMS = 4;
const int DELAY = 500;

const int PINS[4] = { 8, 9, 10, 11 };
int pinDelays[4] = { 0, 0, 0, 0 };

void setup() {
  for (int i = 0; i < NUMBER_OF_DRUMS; i++) {
    pinMode(PINS[i], INPUT);
  }
  Serial.begin(57600);
}

void loop() {
  for (int i = 0; i < NUMBER_OF_DRUMS; i++) {
    if (digitalRead(PINS[i]) == HIGH && pinDelays[i] < 1) {
      Serial.print("drum,");
      Serial.println(i);
      pinDelays[i] = DELAY;
    }
    if (pinDelays[i] > 0) {
      pinDelays[i] -= 1;
    }
  }
}

Note the use of pinDelays to stop the Arduino sending too many signals to the Raspberry Pi. Every time the Arduino sends a signal, it sets pinDelays to a large value. Every time through the loop, it reduces that value by one. It will only send a new signal if the pinDelays has been reduced to zero.

<test your project>
Open the serial port monitor in the Arduino environment and tap the speakers. Do you get messages when you tap one of the drums? You may have to tap them quite sharply, but be careful not to bend them. Do you get different messages for different drums? Do you get a message for each drum? Do the readings stop when you don't tap anything?
## Assemble the drums
This is easy. Just put a ring of plasticine around the rim of each drum to hold it in place. Make sure the metal disk isn't touching the table: it make the drum more sensitive.

<test your project>
Open the Arduino serial port monitor again if you closed it earlier. Do the drums still work?

# Step 5: Update the Python translator
Change the DEVICES = line at the top of the Python script to refer to your new Arduino. If your two devices are /dev/ttyACM0 and /dev/ttyACM1, the line should read:
DEVICES = ['/dev/ttyACM0', '/dev/ttyACM1']

<test your project>
Ensure Scratch is still running the miniband script then run
python music-maker-handler.py

Wait for it to connect to both Scratch and the Arduinos. Then tap the drums and watch the output. You should get something like this:

INFO:root:Instrument: drum, Value: 0
INFO:root:broadcast cymbal
INFO:root:Instrument: drum, Value: 1
INFO:root:broadcast hihat
INFO:root:Instrument: drum, Value: 2
INFO:root:broadcast slowdrum
INFO:root:Instrument: drum, Value: 3
INFO:root:broadcast snare

If it doesn't work, check that Scratch is running and that you've got the correct names for your Arduino devices. (Use dmesg to check after you unplug them and plug them in again.)

# Step 6: Update the Scratch player
1. Create a new sprite called drum. Use the standard Scratch drum costume.
2. Import into drum the sounds miniband/cymbal, miniband/hihat, miniband/slowdrum, and miniband/snare.
3. Create these scripts:
4. Make sure the Python translator script is running.

<test your project>
Double-click on each of the drums scripts in Scratch. Do you hear the right sound? Now tap the drums instrument you made. Do you hear the sound? Does you still see extra "broadcast slowdrum" lines when you tap them them?

# Step 7: Make the guitar

You will need:
Arduino
Breadboard
strip potentiometer
Jumper leads
One 10KΩ resistor
Pencil
Straw
Card

## Wire up the guitar
1. Connect the potentiometer to three long jumper leads. Plug the other ends into three different tracks on the breaboard.
2. Use a jumper lead to connect the +5V pin on the Arduino to one of the outer terminals of the potentiometer
3. Use a jumper lead to connect the GND pin on the Arduino to the other outer terminal of the potentiometer
4. Use a jumper lead to connect the A0 analogue pin on the Arduino to the centre terminal of the potentiometer
5. Connect a 10KΩ resistor between the centre and GND terminals of the potentiometer

## Install the Arduino code

Open the Arduino environment on the Raspberry Pi and add this script:
a
const int THRESHOLD = 10;
const int GUITAR_PIN = A0;
const int PINLIMIT = 5000;

int val;
int pinDelay;

void setup() {
  Serial.begin(57600);
}

void loop() {
  val = analogRead(GUITAR_PIN);
  if (val >= THRESHOLD && pinDelay < 1) {
    Serial.print("guitar,");
    Serial.println(val);
    pinDelay = PINLIMIT;
  }

  if (pinDelay > 0) {
    pinDelay = pinDelay - 1;
  }
}

Save the script
Upload the script to the Arduino

<test your project>
Open the serial port monitor in the Arduino environment and press the potentiometer at different places. Do you get different readings appear in the serial port monitor? Do the readings stop when you stop pressing?
## Assemble the guitar
1. Draw a guitar shape on the card. Colour it in and cut it out. It needs to be large enough that the strip potentiometer fits on the neck of the guitar.
2. Stick the pencil to the back of the guitar to stiffen it. You need to make sure that the pencil goes all the way along the neck.
3. Stick the potentiometer to the fretboard of the guitar.

<test your project>
Open the serial port monitor again if you closed it earlier. Does the guitar still work? Do you still get different readings when you press the guitar in different places? Does the output stop when you're not touching it?

# Step 8: Update the Python translator
Change the DEVICES = line at the top of the Python script to refer to your new Arduino. If your devices are /dev/ttyACM0, /dev/ttyACM1, /dev/ttyACM3, nd the line should read:
DEVICES = ['/dev/ttyACM0', '/dev/ttyACM1', '/dev/ttyACM3']

<test your project>
Ensure Scratch is still running the miniband script then run
python music-maker-handler.py

Wait for it to connect to both Scratch and the Arduinos. Then tap the press the potentiometer and watch the output. You should get something like this:

INFO:root:Instrument: guitar, Value: 260
INFO:root:sensor-update guitar_pitch 25
INFO:root:broadcast guitar
INFO:root:Instrument: guitar, Value: 75
INFO:root:sensor-update guitar_pitch 7
INFO:root:broadcast guitar
INFO:root:Instrument: guitar, Value: 898
INFO:root:sensor-update guitar_pitch 87

If it doesn't work, check that Scratch is running and that you've got the correct names for your Arduino devices. (Use dmesg to check after you unplug them and plug them in again.)

# Step 9: Update the Scratch player
1. Create a new sprite called guitar. Use the standard miniband/guitar costume.
2. Import into drum the sounds miniband/cymbal, miniband/hihat, miniband/slowdrum, and miniband/snare.
3. Create these scripts:
4. Make sure the Python translator script is running.

<test your project>
Double-click on each of the drums scripts in Scratch. Do you hear the right sound? Now tap the drums instrument you made. Do you hear the sound? Does you still see extra "broadcast slowdrum" lines when you tap them them?

# Step 10: Rock out!
Your miniband works! Rock!

from array import *
import threading
import socket
import time
import sys
import struct
import serial
import io
import datetime as dt
import logging

PORT = 42001
DEFAULT_HOST = '127.0.0.1'
BUFFER_SIZE = 240 #used to be 100
SOCKET_TIMEOUT = 1
DEVICES = ['/dev/ttyACM0']
ARDUINO_BAUD_RATE = 57600

BROADCAST_NAMES = {'guitar': 'guitar',
    'drum': {0: 'cymbal',
        1: 'hihat',
        2: 'slowdrum',
        3: 'snare',
        4: 'tomtom'},
    'maracas': 'maracas'}

SENSOR_NAMES = {'guitar': 'guitar_pitch'}

logging.basicConfig(level = logging.INFO)

class MyError(Exception):
    def __init__(self, value):
        self.value = value

    def __str__(self):
        return repr(self.value)

class ScratchSender(threading.Thread):
    def __init__(self, socket):
        threading.Thread.__init__(self)
        self.scratch_socket = socket
        self._stop = threading.Event()

    def join(self,timeout=None):
        self._stop.set()
        threading.Thread.join(self, timeout)

    def stopped(self):
        return self._stop.isSet()

    def run(self):
        while not self.stopped():
        time.sleep(0.01) # be kind to cpu - not certain why :)

    def send_scratch_command(self, cmd):
        n = len(cmd)
        a = array('c')
        a.append(chr((n >> 24) & 0xFF))
        a.append(chr((n >> 16) & 0xFF))
        a.append(chr((n >> 8) & 0xFF))
        a.append(chr(n & 0xFF))
        self.scratch_socket.send(a.tostring() + cmd)

class ArduinoListener(threading.Thread):
    def __init__(self, device, speed, sender, instruments, values):
        threading.Thread.__init__(self)
        self.arduino_device = serial.Serial(device, speed, timeout=0.5)
        self._stop = threading.Event()
        self.scratch_sender = sender
        self.instruments = instruments
        self.values = values

    def join(self,timeout=None):
        self._stop.set()
        threading.Thread.join(self, timeout)

    def stopped(self):
        return self._stop.isSet()

    def run(self):
        self.arduino_device.readline() # discard the first (partial) line
        while not self.stopped():
        logging.debug('Thread waiting for a signal')
        try:
        device_line = self.arduino_device.readline()
        if device_line :
        instrument, instrument_value_string = device_line.rstrip().split(',', 1)
        instrument_value = int(instrument_value_string)
        logging.info('Instrument: %s, Value: %d' % (instrument, instrument_value))
        if instrument in self.values:
        try:
        logging.info("sensor-update %s %d" % (self.values[instrument], (instrument_value * 100) / 1024))
        self.scratch_sender.send_scratch_command("sensor-update %s %d" % (self.values[instrument], (instrument_value * 100) / 1024))
        except KeyError:
        # Do nothing
        pass
        if isinstance(self.instruments[instrument], dict):
        broadcast = self.instruments[instrument][instrument_value]
        else:
        broadcast = self.instruments[instrument]
        try:
        logging.info("broadcast %s" % broadcast)
        self.scratch_sender.send_scratch_command('broadcast %s' % broadcast)
        except KeyError:
        # Do nothing
        pass

        except serial.SerialException:
        logging.error('Serial exception')
        logging.debug('Thread run() exiting')

def create_socket(host, port):
    while True:
        try:
        logging.info('Connecting to Scratch')
        scratch_sock = socket.socket(socket.AF_INET, socket.SOCK_STREAM)
        scratch_sock.connect((host, port))
        break
        except socket.error:
        logging.warning("There was an error connecting to Scratch!")
        logging.warning("I couldn't find a Mesh session at host: %s, port: %s" % (host, port) )
        time.sleep(3)
    return scratch_sock

def cleanup_threads(threads):
    logging.debug("Stopping %d threads" % len(threads))
    for thread in threads:
        thread.join()
    logging.debug("Threads joined")

if __name__ == '__main__':
    if len(sys.argv) > 1:
        host = sys.argv[1]
    else:
        host = DEFAULT_HOST

cycle_trace = 'start'
while True:
    if (cycle_trace == 'disconnected'):
        logging.info("Scratch disconnected")
        cleanup_threads(listeners + sender)
        time.sleep(1)
        cycle_trace = 'start'

    if (cycle_trace == 'start'):
        # open the socket
        logging.info('Connecting to Scratch...')
        the_socket = create_socket(host, PORT)
        logging.info('Connected to Scratch')
        the_socket.settimeout(SOCKET_TIMEOUT)
        sender = ScratchSender(the_socket)
        listeners = [ArduinoListener(device, ARDUINO_BAUD_RATE, sender, BROADCAST_NAMES, SENSOR_NAMES) for device in DEVICES]
        cycle_trace = 'running'
        logging.info("Listeners running....")
        sender.start()
        for listener in listeners:
        listener.start()

    # wait for ctrl+c
    try:
        #just pause
        time.sleep(0.1)
    except KeyboardInterrupt:
        logging.warning("Interrrupted")
        cleanup_threads(listeners + [sender])
        sys.exit()